## Slide 1: Link creation and modification via connectivity-service
Nigel Davis
20250422

## Slide 2: Rough proposal
Use connectivity-service to create a link between two points to support a connection of the layer-rate identified
  This is essentially requesting the connectivity service below the link and to cause a link of the selected layer with NEPs that support the identified qualifier
  The key layer of concern has a connection in the sub-media layer
The link details would be via “pacs” augments, taken from the link details

## Slide 3: Other connectivity-service considerations
Multiple services in parallel (service-set)
  May simply be parallel creation with no subsequent association
  May be associated in a set or other more complex structure
Trial service returned details via streaming but not committed to the network
  Temporary reserve of resources until service either committed to network or deleted
  No reserve of resources beyond calculation activity (so auto delete of service)
    Note that during the computation the resources may be acquired and then released after computation
Timed service creation
  With delayed commit to the network
  With a fully fledged temporal model
Path set creation during service creation
Path set creation during trial service activity
  This may be a proposed path set that is deleted after the trial or is maintained after the trial
Multi-layer service creation (where the NEPs do not exist prior to the creation and are simply implied by the SIPs)

## Slide 4
From otcc2020.ND.010_TAPI-ConnectivityServiceComputationService
at https://github.com/Open-Network-Models-and-Interfaces-ONMI/TAPI-Activities/blob/main/ContributionsForDiscussions/otcc2020.ND.010_TAPI-ConnectivityServiceComputationService.pptx

## Slide 5: Complex workflows
Parallel simultaneous need to be built in one coherent operation
  Choices for multi-layer build workflow are primarily proprietary
For alternative, first alternative needs to be built then removed prior to next alternative
  Alternatives will be streamed as built and then deleted
    There needs to be some form of progress indication (this is essentially the progress of the task – perhaps take/enhance oam-job state and maybe even add an optional oam-jobs to connectivity-service operation)
The “context” of the build is challenging especially where some services are expected to have been deleted prior to the requirement for the new services
For full support
  Needs to have temporal+ model
  May need to provide indication of which infrastructure to use

## Slide 6: Diagrams