## Slide 1
The following slides are work in progress. This pack focusses on the modelling of the interconnect between the plug and the host.

## Slide 2: Primary consideration – reporting alarms and PMs
Simplified model
Per-client-signal – normal alarms against client
Per-lane – requires special treatment
  Min/Max/Average
    Low/High
      Warning/Fail (called Alarm)
The per-lane conditions point to a composite condition name
  This has been explored several times in the past (e.g., back in ~2002 Nortel made a proposal to ITU-T on this)…
  The current structure does not lend itself well to this as it stands as there is an enum for the condition
    The detected condition qualifier could be used for the structured content. The qualifier comment is
      Further information necessary to precisely/uniquely/unambiguously identify the Condition Detector.
      For Equipment and Processing Alarm Category, e.g. the local id of the ActualNonFieldReplaceableModule which identifies exact alarm source.
      For Environment Alarm Category, e.g. on the same Device instance may appear more Environmental alarm notifications with same Alarn Name.
      For Connectivity Alarm Category in case that same CEP instance includes e.g. both OTS and OMS monitoring layers.
The per-lane conditions example:
  Pre-FEC BER Minimum Host Input (Data Path Lane1) - Low Warning
  This becomes:
    detected-condition-name: PRE_FEC_BER
    detected-condition-qualifier: Lane-1 Minimum Low Warning (and Lane-2 Maximum High Fail… etc.)
To avoid complex modelling, these could be reported against
  the plug equipment
  Per lane access-ports
  Per-lane CEPs that are disconnected from the line side structure
Or just Lane X fail

## Slide 3: TAPI and IETF considerations
TAPI is validating and enhancing support for ZR/ZR+ plugs
  Currently TAPI only exposes lineside properties
In IETF an activity has been exploring plug support
  This has focussed on lineside properties
In both of the above there is an assessment of need for support modelling of electrical lanes
  Taking the general modelling approach applied, neither TAPI nor IETF would consider supporting the lanes (these are equivalent to backplane and backplane is normally abstracted away)
The challenge in the case of lanes is
  This is an inter-vendor interconnect
  The lanes exist between a L3 control domain and a L1/0 control domain and hence at the bridge between a TAPI representation and an IETF representation
    In the TAPI group we have been looking at providing a relationship between the TAPI and IETF models. This is targeted at TAPI 2.7 and could be back propagated to 2.5.x
Why modelling lanes might be relevant
  Potential incompatibility between plug and host lane settings (inter-vendor issue)
    This can be abstracted
  FEC measurements available that may help diagnose inter-vendor issues
    This cannot be easily abstracted, but probability of an issue once type compatibility has been validated is very low for specific settings
Question:
  Is direct access to lane management-control parameters necessary?
  What level of abstraction seems relevant?
  Should this be a TAPI model, and IETF model or both?

## Slide 4: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Plug
Router hardware
Internal detail

## Slide 5: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
y
x
Should be single signal as lanes not visible to peer 
But if multiple clients, this would be visible and may under some cases be 1:1 with the lanes…. This is NOT a representation of the lanes.
Not this
Plug
Router hardware
Internal detail

## Slide 6: The model for plug lanes
  The plug – host interface appears equivalent to backplane and hence would normally not be modelled
    The internal physical structure is abstracted away using principles developed by ITU-T in the 1980s
  BUT a plug from one vendor is placed a device from another.
    There is therefore an inter-vendor interconnect that may need to be policed and hence visible
    Properties such as FEC may need to be monitored or minimally accessed if there is an issue
  The lane interface is configurable but configuration can be conveyed via profiles to plug and router so detail do not need to be visible
    The profile could be set per plug instance
  The plug interface is split between router and plug (obviously). The router is visible via IETF interface and the Plug via TAPI. The split of standards makes modelling more complex.
    The TAPI model would follow normal TAPI principles and hence be systematic with other modelling.
    The IETF models do not have such consistent principles, but TEAS etc. could be used to help pattern formation (or a TAPI-like model could be created in IETF)
  Visibility could be achieved via CLI, but that would require complex node access.
    Suggest either no visibility or visibility via NBI

## Slide 7: Background and partially obsolete material

## Slide 8: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Standard TAPI modelling…
Internal structure ignored
Ethernet projected to edge
Plug
Router hardware
Internal detail
Ethernet
TAPI
IETF
IETF-TAPI Linkage
DSR

## Slide 9: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Standard TAPI modelling…
Internal structure ignored
Ethernet projected to edge
Plug
Router hardware
Internal detail
Projection
TAPI
IETF
IETF-TAPI Linkage (peer)
DSR
Ethernet
DSR

## Slide 10: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
HOST / ROUTER
HOST LANES
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Plug
Router hardware
DSR
IMA
DSR
Access Ports
Physical Span
DSR
DSR
DSR
Physical Medium Attachment (PMA) / Electrical Interface:
The physical connection consists of 8 electrical lanes (400GAUI-8).
Each lane uses 50G PAM4 (Pulse Amplitude Modulation 4-level) signaling.
E.g., 400GbE (400 Gigabit Ethernet)
FEC / Mapping Layer
E.g., Concatenated FEC (C-FEC)
Physical Coding Sublayer (PCS):
Standard IEEE 802.3 PCS is used for 400GBASE-R.
Functions include 64B/66B encoding, scrambling, and lane distribution (Inverse Mux).

## Slide 11: ZR/ZR+ Considerations
We can break the problem down into three separate considerations
  The model for the ZR/ZR+ optics including layer choices and specific properties – this is clearly necessary
  The model for the plug lanes
    May be necessary:
      Inter-vendor boundary
    May not be necessary:
      It is internal tracking that corresponds to “backplane” in other contexts
  The split between TAPI for L0/L1 and IETF for L3
    If the lanes are to be modelled, who would model them?
    The underpinning of the split of responsibility is layer but that is conflated with IP device v photonic device is often conflated
This document focusses on (2) and (3).
Options:
  Single abstracted proxy TP representing the 8 lanes v 8 separate TPs, one per lane, each to pins and via strands over the access port and span v 8 TPs but no strands and just links (no pin numbers etc.)
  Full stack v shallow stack (previously we got burnt with shallow stack )

## Slide 12: OIF-400ZR 400GBASE-R
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMCA
OTSiMC
DSR
HOST / ROUTER
OIF-400ZR-02.0:
400GBASE-R, FlexO-4-DSH, and 400ZR frames have similar structures. The 400ZR frame OH area is the same as the FlexO-4-DSH, however, fewer OH fields are defined as required for 400ZR than for FlexO-4-DSH. Bonding across multiple PHYs is not supported by the 400ZR frame structure.
The 400GBASE-R is asynchronously mapped into a 400ZR container using GMP.
The chapter “8.9 400ZR Error Detection and Signaling” lists the alarms
HOST LANES
OLD SLIDE BY ANDREA
Note the use of PHOT:OTSiMCA l-p-q as a CEP contained by a DSR NEP
We would not normally model the backplane… BUT….
The lane consideration is important at vendor boundary.
It is not shown correctly in the model sketch

## Slide 13: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
y
x
Should be single signal as lanes not visible to peer 
But if multiple clients, this would be visible and may under some cases be 1:1 with the lanes…. This is NOT a representation of the lanes.
Not this
Plug
Router hardware
Internal detail

## Slide 14: 4 x 100G multiplexed and carried over a ZR400 payload
100G Connectivity Service
100G Connectivity Service
100G Connectivity Service
100G Connectivity Service
PHOTONIC
OTS_MEDIA
PHOTONIC
OTSiMC
(+OTSi if O/E/O)
Transceiver1
DSR
DSR
OTSiMC Top Connection
MC Connectivity Service
OTSiMCA Connectivity Service
DSR
ODU
(+OTU)
OTSiMCA
OTSiMCA Top Connection
DSR_100G
DSR 100G Top Connection
Things to consider:
What layer-protocol-constraints could be added to the CSEP to express that ZR400 (supporting mux) is required?
  There are no layer-protocol-constraints defined in tapi-dsr.yang
  Or is it sufficient to specify the required profile?
Can all relevant alarms and PMs be modelled against the OTSiMC CEP? Or, are there ZR/ZR+ specific alarms/PMs to be considered on the OTSiMCA CEP?
DSR does not define l-p-q for rates above 400G.
  I think it is better to add l-p-q identities for 500G to 1200G, 1600G, and 3200G

## Slide 15: 400G carried over a ZR400 payload
400G Connectivity Service
PHOTONIC
OTS_MEDIA
PHOTONIC
OTSiMC
(+OTSi if O/E/O)
Transceiver1
DSR
DSR
OTSiMC Top Connection
MC Connectivity Service
OTSiMCA Connectivity Service
DSR
ODU
(+OTU)
OTSiMCA
OTSiMCA Top Connection
DSR_400G
DSR 400G Top Connection

## Slide 16: ZR/ZR+ Considerations
We can break the problem down into three separate considerations
  The model for the ZR/ZR+ optics including layer choices and specific properties – this is clearly necessary
  The model for the plug lanes
    May be necessary:
      Inter-vendor boundary
    May not be necessary:
      It is internal tracking that corresponds to “backplane” in other contexts
  The split between TAPI for L0/L1 and IETF for L3
    If the lanes are to be modelled, who would model them?
    The underpinning of the split of responsibility is layer but that is conflated with IP device v photonic device is often conflated
This document focusses on (2) and (3).

## Slide 17: The model for plug lanes
  The plug – host interface appears equivalent to backplane and hence would normally not be modelled
    The internal physical structure is abstracted away using principles developed by ITU-T in the 1980s
  BUT a plug from one vendor is placed a device from another.
    There is therefore an inter-vendor interconnect that may need to be policed and hence visible
    Properties such as FEC may need to be monitored or minimally accessed if there is an issue
  The lane interface is configurable but configuration can be conveyed via profiles to plug and router so detail do not need to be visible
    The profile could be set per plug instance
  The plug interface is split between router and plug (obviously). The router is visible via IETF interface and the Plug via TAPI. The split of standards makes modelling more complex.
    The TAPI model would follow normal TAPI principles and hence be systematic with other modelling.
    The IETF models do not have such consistent principles, but TEAS etc. could be used to help pattern formation (or a TAPI-like model could be created in IETF)
  Visibility could be achieved via CLI, but that would require complex node access.
    Suggest either no visibility or visibility via NBI

## Slide 18: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Standard TAPI modelling…
Internal structure ignored
Ethernet projected to edge
Plug
Router hardware
Internal detail
Ethernet
TAPI
IETF
IETF-TAPI Linkage
DSR

## Slide 19: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
DSR
PHOT
OTS_MEDIA
PHOT
V1
PHOT
IMA
OTSiMC
DSR
HOST / ROUTER
HOST LANES
DSR
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Standard TAPI modelling…
Internal structure ignored
Ethernet projected to edge
Plug
Router hardware
Internal detail
Projection
TAPI
IETF
IETF-TAPI Linkage (peer)
DSR
Ethernet
DSR

## Slide 20: OIF-400ZR 400GBASE-R - 400G carried over a ZR400 payload
Router functions
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
HOST / ROUTER
HOST LANES
DSR
DSR
?
PHOT
OTS_MEDIA
PHOT
V1
PHOT
OTSiMC
Plug
Router hardware
DSR
IMA
DSR
Access Ports
Physical Span
DSR
DSR
DSR
Physical Medium Attachment (PMA) / Electrical Interface:
The physical connection consists of 8 electrical lanes (400GAUI-8).
Each lane uses 50G PAM4 (Pulse Amplitude Modulation 4-level) signaling.
E.g., 400GbE (400 Gigabit Ethernet)
FEC / Mapping Layer
E.g., Concatenated FEC (C-FEC)
Physical Coding Sublayer (PCS):
Standard IEEE 802.3 PCS is used for 400GBASE-R.
Functions include 64B/66B encoding, scrambling, and lane distribution (Inverse Mux).

## Slide 21
Options:
  Single abstracted proxy TP representing the 8 lanes v 8 separate TPs, one per lane, each to pins and via strands over the access port and span v 8 TPs but no strands and just links (no pin numbers etc.)
  Full stack v shallow stack (previously we got burnt with shallow stack )