## Slide 1: Ivy Hackathon
Nigel Davis (Ciena)
20260603

## Slide 2: Overview
Hackathon architecture
Ivy model
Objectives of Hackathon
Sketch of possible arrangements
Prior to Hackathon
Vision
What will not be explored

## Slide 3: Hackathon Architecture
Configuration:
  A controller from one vendor plays the role of inventory system (inventory role)
  Several controllers from different vendors are connected to the inventory controller (controller role)
  Each controller role provides a view of network elements and their physical inventory
Multiple vendors engage in various orientations
Interconnect in various configurations
Any appropriate vendor system can take the inventory role
The Use Case will be alignment via GET (notification will not be exercised at this stage)
Inventory role
Controller role
Controller role
Network
Network
May be:
Controller
Orchestrator
Inventory system
Network may be:
An image in the controller
A simulation
Real hardware
ivy
Ideally network elements would be a mix of IP, Ethernet, OTN and optical where there were various NEs of different mixes of capabilities. This should have no impact on the ivy interface capability
Note that this follows on from the successful
IETF125 Hackathon demonstration of IVY
Display of inventory
Display of inventory
Compare Content

## Slide 4: Ivy model
Useful links
IETF | IETF 126 Hackathon
IETF 126 Hackathon | IETF Community Wiki (see YANG Data Model for Network Inventory (IVY) – 2)
Network Inventory YANG (ivy)
draft-ietf-ivy-network-inventory-yang-18 - A Base YANG Data Model for Network Inventory
ietf-ivy-wg/network-inventory-yang
The key structure is component
Component represents equipment, holder, pluggable etc.
Most properties are clear in meaning
  For holder, most properties are not required
Compared to TAPI
  The model does not support expectation/actual split
  There is not access-port or physical-span
Need to do a property by property comparison of tapi-equipment to determine precisely what is missing
module: ietf-network-inventory
+--ro network-inventory
+--ro network-elements
+--ro network-element* [ne-id]
+--ro ne-id string
+--ro ne-type? identityref
+--ro uuid? yang:uuid
+--ro name? string
+--ro alias? string
+--ro description? string
+--ro software-rev* [name]
| +--ro name string
| +--ro revision? string
| +--ro patch* [revision]
| +--ro revision string
+--ro mfg-name? string
+--ro product-name? string
+--ro product-rev? string
+--ro components
+--ro component* [component-id]
+--ro component-id string
+--ro class union
+--ro uuid? yang:uuid
+--ro name? string
+--ro alias? string
+--ro description? string
+--ro software-rev* [name]
| +--ro name string
| +--ro revision? string
| +--ro patch* [revision]
| +--ro revision string
+--ro mfg-name? string
+--ro product-name? string
+--ro hardware-rev? string
+--ro mfg-date? yang:date-and-time
+--ro part-number? string
+--ro serial-number? string
+--ro asset-id? string
+--ro is-fru? boolean
+--ro uri* inet:uri
+--ro parent*
| -> ../../component/component-id
+--ro parent-rel-pos? string
+--ro is-main? boolean

## Slide 5: Objectives of Hackathon
Demonstrate that systems can connect
  Prove this prior to the actual hackathon to save wasted time
Demonstrate ivy can convey inventory
  Partly exercise this prior to actual hackathon, again to save wasting time
Exercise inventory detail
  Get all inventory then display
Explore for missing detail
  Compare display on inventory role with display on controller role devices
Add properties to model and convey new data
Compare with TAPI and add further properties where obvious
Highlight discrepancies
Consult operators on relevance of shortfalls
Propose additions to IVY as appropriate
This is a validation of the use of ivy equipment.
The activity will NOT cover Topology models, Service models, IP capabilities, Photonic capabilities… Etc.

## Slide 6: Sketch of possible arrangements
Vendor W brings a controller that can perform both roles
Vendor X brings two distinct controllers one for inventory role and one for controller role
Vendor Y only brings an inventory solution
Vendor Z brings a controller that supports the controller role
 | Controller role | Inventory role | 
Config 1 | W, Xc, Z | W | 
Config 2 | W, Xc, Z | Xi | 
Config 3 | W, Xc, Z | Y | 
One or more vendors may also have a TAPI equipment capability
Single vendor or multi-vendor interconnect may be achievable
Comparison of information transferred by TAPI may be of value

## Slide 7: Prior to hackathon
In ivy
  Agree use cases as described in these slides
  Agree interaction formats etc.
Participants
  Determine which systems will be used
  Identify design resources to be on site
  Develop/refine NBI and SBI as appropriate
  Validate interconnect with other vendors via various pairwise interactions
    Simply connect
    Try a get

## Slide 8: Vision
Currently the IVY model provides less than TAPI and TAPI uses some more compact modelling patterns
Through the Hackathon and via consultation with operators, add to IVY to cover gaps such that IVY covers all relevant capabilities of TAPI
Refine the IVY model to align with TAPI patterns where agreed
Demonstrate equivalence in parallel TAPI/IVY interfacing
Build prototype TAPI with IVY equipment
Demonstrate migration opportunity (using CoPilot/LLMs to assist in code and documentation)
Define value-justified steps (vendors and operators)
Coordinate migration from TAPI Equipment to IVY Equipment across the industry
Consider OC advancements in a similar way

## Slide 9: What will not be explored
Topology models and interconnect between systems exposing topology
Service models
IP capabilities
Photonic capabilities

## Slide 10: Questions?